Research Proposal for the 5th IAEA JOINT EXPERIMENT

From:	Gennadii Vorobjev, Nikolai Timofeev, St. Petersburg State University

Date:	15 July 2012

(Joint Experiment will be held on September 10- 14, 2012)

Proposed Research Topic:

Installation and investigation of RF pre-ionisation on GOLEM tokamak

Purposes:

To install and test low-power ECR preionization for plasma formation on GOLEM tokamak

Background:

Optimisation of the use of HTS PF coils on GOLEM requires modifications to the discharge scenario. To reduce AC losses during current ramp-up in HTS coils, reduction in the current ramp-up speed is needed, as this will result in a slower ramp-up of the current in coils. One of possible solutions may be reduction in the loop voltage needed for the plasma breakdown. It is well known that RF pre-ionisation is a powerful tool to achieve this goal [1].

Scope:

We propose to install a low-power magnetron at the EC fundamental harmonics for the toroidal field of ~ 0.1T at 2.45GHz, ~1kW injected power. This RF power will be applied in a short (<1ms) pulse during the TF ramp-up and should be sufficient to create an RF plasma which will reduce requirements for the breakdown electric field.

Method:

- Manufacture of pre-ionisation system using a low-price kitchen microwave oven. It will be de-assembled and the magnetron and other components will be used. This will take 1-2 days and requires a workshop space with basic tools. All work will be done by proposers.

- Installation of the magnetron ~1m away from the tokamak, at equatorial plane, with the end of the waveguide attached to the midplane glass window. Some RF shielding will be installed to prevent radiation.

- Experimental investigation of RF pre-ionisation on GOLEM tokamak. About 20-30 plasma pulses will be needed to optimise parameters. Can be done in one or two sessions, possibly in parallel with other experiments.

Needed equipment:

- Two cheapest microwave ovens (one is not sufficient for the system). The preferred make will be specified, the cheapest with manual controls is preferred.

- Thyristor switch for 5kV (will be provided by proposers)

- Waveguide and antenna (will be provided by proposers)

- Capacitor 5kV, 10mkF (will be provided by proposers)

- Support system for the magnetron and waveguide.

- References:

- B Lloyd at al, NF 31 (1991) 2031