Measurements of plasma parameters by the Ball Pen and Langmuir probes on the GOLEM tokamak

Vojtech Svoboda1, Jan Stockel2, Jiri Adamek2, Miglena Dimitrova2

1Faculty on Nuclear Sciences and Physical Engineering, Czech Technical University in Prague, Czech Republic, svoboda@fjfi.cvut.cz

2Institute of Plasma Physics, Czech Academy of Sciences, Prague, Czech Republic, stockel@ipp.cas.cz, adamek@ipp.cas.cz, dimitrova@ipp.cas.cz

The GOLEM tokamak, (R = 0.4 m, a = 0.085 m), operates currently at a modest range of parameters: Bt < 0.6 T, Ip < 8 kA, discharge duration ~ 20 ms [1]. Recently it has been equipped with the probe head combining the Ball-pen probe (BPP) [2] and the Langmuir probe (LP) with the aim to measure directly the plasma potential and the electron temperature with a sufficiently high temporal resolution.

This contribution summarized achieved experimental results on measurement of the electron temperature and plasma potential by several way.

- The electron temperature Te is determined from classical fitting of the IV characteristics measured the Langmuir probe;

- Alternatively, Te and the plasma potential are derived from the same data using approach based on the first derivative technique [3].

- Results are compared with the directly measured plasma potential by BPP and Te measurements from the combined BPP+LP.

Agreement is satisfactory, and observed differences are discussed.

V. Svoboda et al.  Fusion Engineering and Design, 86(6-8):1310–1314, 2011.

Adámek, J. et al; Czechoslovak Journal of Physics, 2004, 54 (3): 95–99.

Ts Popov et al, Plasma Sources Sci. Technol. 25 (2016) 033001,

This is the last possible line of text to leave a 1 inch bottom margin. No page number.