Application of Scintillation Detectors for Investigation of Runaway Electrons at COMPAS tokamak

J. Cerovsky1,2, O. Ficker1,2, E. Macusova1, J. Mlynar1,2, V. Svoboda1, L. Lobko1, J. Caloud1,2,

V. Weinzettl1

1 Institute of Plasma Physics of the CAS, Prague, Czech Republic

2 FNSPE, Czech Technical University in Prague, Prague, Czech Republic

The generation of runaway electrons in tokamaks has been in recent years recognized as threat for operation of future experimental devices and runaway electron physics has gained attention of many fusion scientist, who are trying to shed light on generation mechanisms

or finding a safe way of runaway electron suppression.

In last few years runaway electrons have been extensively studied at COMPASS tokamak [1], which turn out to be good test bed for investigation of runaway electron physics due to its size and safe operation during runaway electron experiments [2]. At COMPASS tokamak generation mechanisms, various mitigation strategies including massive gas injection and solid state pellet injection were explored. Great emphasis was put on investigation of methods of generation and mitigation of so called  runaway electron beams and determination of their properties [3].

Various diagnostic methods were developed for investigation of runaway electrons and many of them are based on detection of radiation, which is caused by interaction of relativistic electrons with material. Detection and spectroscopy of resulting bremstrahlung radiation can provide useful information needed for characterization of runaway electrons.

Aim of this contribution is a description of runaway electron experiments carried out

at COMPASS tokamak and application of scintillation detectors in runaway electron studies. Experimental setup and used detectors during experimental campaigns will be discussed. Analysis of acquired from scintillation detectors will be shown and put into context

of runaway electron research at COMPASS tokamak.

Acknowledgement: The work has been supported by the Operational programs RDE

CZ.02.1.01/0.0/0.0/16\_019/0000778: Centre of Advanced Applied Sciences. This work has been supported by MEYS projects LM2015045 and carried out within the framework of the EUROfusion Consortium. It has also received funding from the Euratom research and training program 2014-2018 and 2019-2020 under grant agreement No 633053 with the Co-fund by MEYS project number 8D15001. The views and opinions expressed herein do not necessarily reflect those of the European Commission. This work was also supported by the Grant Agency of the Czech Technical University in Prague, grant No. SGS19/180/OHK4/3T/14.

[1] Panek R. et al. 2016 Plas. Phys. Contr. Fusion 58 014015
[2] Mlynar J. et. al. 2019 Pls. Phys. Contr. Fusion 61 014010

[3] Ficker O. et. al. 2019 Nucl. Fusion 59 096036