The BME Lectures - Tokamak Engineering - “How to Operate a Tokamak” T N Todd
Tom Todd & Mikhail Gryaznevich UKAEA-Euratom Association, Culham Science Centre
COMPASS-D
This work was funded by the UK DTI and by EURATOM.
How to Operate a Tokamak

---
Machine Preparation
Electrical engineering
Mechanical structure
Vacuum and gas systems
Diagnostics and data acquisition
Control system and Operating Instructions
Safety systems
Necessary Diagnostics
Engineering
Loop voltage
Toroidal plasma current
Plasma position
Interferometer
Impurity survey spectrometer
Plasma Initiation
Stray magnetic fields
Gas breakdown and current rise
Contents

---
Plasma Operating Limits
Current
Density
Pressure (beta)
Edge Localised Modes
Performance predictions
Plasma duration
Confinement
Current drive
Human Factors
Operations Planning
Team building
Safety
Contents

---
Electrical engineering
Coil selection
current directions!
turns ratios
mutual inductance cancellation
Joint resistances
bus-bars
selection links
machine assembly
Insulation resistance
Cooling systems
coils (insulation failure)
ignitrons (mercury redistibrutes)
Switch timing sequence
Otherwise……

---
Electrical engineering
Coil selection
current directions!
turns ratios
mutual inductance cancellation
Joint resistances
bus-bars
selection links
machine assembly
Insulation resistance
Cooling systems
coils (insulation failure)
ignitrons (mercury redistibrutes)
Switch timing sequence
Otherwise……
Spectacular failure!

---
Mechanical structure
“Housekeeping”: remove debris and tools from….
machine (exterior)
torus (interior: may need special tools)
bus-bars
machine vicinity (range of dipole field)
Bolt torques: check….
coil supports
electrical joints
machine assembly

---
Vacuum and gas systems
Ultra High Vacuum Vessel Conditioning - after every opening:
Clean and bake all in-vessel components before installation
Do thorough leak testing
Need to achieve 2 x 10-8 torr
Bake (eg 100 hrs at 150 °C, avoiding cold spots), eg. by:
Poloidal field induction
Toroidal field induction (only suits bellows vessels)
Direct connection across diameter of torus
Hot inert gas blanket
Contact heater pads:
self-regulating semiconductor
traditional resistance wire
Use TMPs, cryopumps or diffusion pumps with cold traps
Don’t forget to pump and bake the UHV gas lines!
Maybe use a palladium foil filter to purify the gas

---
Vacuum and gas systems
Ultra High Vacuum Vessel Conditioning
Use Residual Gas Analyser
Ensure meaningful sampling zone
Provide RGA system baking
Consider pumped “sniffer” orifice for high pressures
Make trend analysis of key masses:
44 CO2 and deuterated acetone fragment
40 evidence of Ar from air leak
32 evidence of O2 from severe air leak
28 mixture of N2 (air leak) and CO (dirty walls)
18 water
17 water fragment
14 N cracking-fraction: check on mass 28 N2
deuterium complicates the hydrocarbons

---
Vacuum and gas systems (Compass RGA)
Evidence of dirty conditions

---
Vacuum and gas systems (Compass RGA)
4
Total
28
18
40
time

---
Vacuum and gas systems (Compass RGA)

---
Vacuum and gas systems
Glow discharge cleaning
not in air or water vapour - check gas source!
helium-methane mix for carbonisation
helium-tri-methyl-borine mix for boronisation
helium to remove hydrogenics from walls etc
Methane and tri-methyl borine are also inflammable!
Or consider gettering, eg with titanium balls or filaments
Check piezo-valve response time and throughput
Consider bias voltage and/or “unsticking” pulse

---
Vacuum and gas systems
Interior of Compass-D,
showing instrumented tiles
and boron carbide coating

---
Vacuum and gas systems
Main working species
hydrogen for economy
deuterium for confinement
helium for low Zeff in dirty machine
If hydrogenic, care with exhaust routing!
Consider 400 °C palladium molecular sieve as working gas filter
Trace gases
neon, silane etc for core spectroscopy
neon, argon etc for radiative mantle experiments
helium-3 etc for minority-species ICRH
carbon-13 methane for wall interaction studies

---
Diagnostics and Data Acquisition
Physical
viewing lines
alignment accuracy
GDC shutters open
windows still clear in relevant waveband
viewing dumps still “black” in relevant band
equipment rigidly fixed (EM forces)
vacuum lines and charge-exchange gas cells OK
Electronic
channel identification
polarities
amplifier and integrator gains
earthing strategy (often compromised)
unintended “pick-up loops” in signal cabling
everything switched on! (NB thermal drift)

---
Diagnostics and data acquisition
Calibration
viewing volume
sensitivity
inter-channel cross-talk
noise amplitude
ADC settings
gains
offsets
sampling rates
definition of time zero! (eg initiation event for Vloop rise)
Video cameras
lens selection
filter selection
recording devices

---
Control system
Event sequence
agree definition of time zero!
allow settling times
core/primary bias
toroidal field (main L/R and eddy currents near diagnostics)
pre-fill gas injection (H2 molecule speed 2km/s)
pre-ionisation
Plant operational limits
single-parameter design maxima
recent commissioning experience, moving from “safe” to maxima
combination parameter design maxima (eg TF x Ip, Paux x time)
hardware (trip) and software limit settings (passwords)
utility demands:
mains dips may affect other users - eg the local town
peak demand affects power bill!

---
Control system(Compass-D Operating Limits)

---
JET Operating Instructions
JET Operating Instructions
Divided into groups by main function:
Note gaps in sequence, due to continuous evolution!

---
JET Operating Instructions
Ripple at outboard mid-plane
Examples
  - 1.1 Disruption Avoidance – Max IPlasma:
    - Expert Session Leader	4.6MA
    - Full License	4.1MA
    - License A	3.1MA
    - License B	2.1MA
    - License C (trainee)	Zero!
1.1 also dictates permissible shapes
Steadily growing list, eg for ITER shapes at higher plasma current
3.1 Toroidal Field limits – Max ITF:
Varies with ripple () %
Bursting force (ITF2)
Temperature gradients (ITF2t)

---
Safety systems
Plant safety interlocks
current limit
voltage limit
ignitron misfire
temperature limit
Environmental safety
toxic gas discharges (pyrolyse, high stack)
explosive/pyrophoric gas leaks and discharges
asphyxiant gas leaks
copper etc in cooling water discharges
Human safety
access interlocks
duplicate with separate system (eg entirely pneumatic)
over-rides should be difficult but possible
Standing Orders (Emergency Instructions)

---
Safety systems: area access door interlocks
pneumatic
electric

---
Engineering
Machine control & protection requires many measurements...
Electrical
coil currents
power supply currents
voltages
connection link positions
Mechanical
vacuum
structural movements
forces/ strains
temperatures
coils
plasma facing components
Necessary Diagnostics

---
Loop voltage: plasma surface, toroidal
The single most important diagnostic of all!
plasma initiation behaviour
current ramp-up behaviour
flat-top confinement indicator
discharge termination behaviour
Normal tokamaks exhibit 1-2 V/turn in flat-top OH discharges
too low
0.4V/t = slideaway discharge (200keV quasi-thermal)
0.05V/t = runaway discharge (10Mev max, Ip-limited)
too high
 3V/t = severe radiative losses or loss of position control
Necessary Diagnostics

---
Loop voltage: plasma surface, toroidal
Positive excursions
loop voltage initiation (timing check)
OH banks firing, or thyristor commutation
plasma current interruptions or resistance increases
decrease in electron temperature
Pogutse-Parail (electron beam) instability
Negative excursions
ramp-down initiation (timing or interlock check)
collapse of internal inductance due to MHD
beneficial electron heating
beneficial current drive
Necessary Diagnostics

---
Loop voltage (Globus)
Minor disruption
Major disruption
Necessary Diagnostics

---
Toroidal plasma current
The other really vital diagnostic!
Excursions (or faltering) as for Vloop but inverted
With Vloop , R, a, κ, Zeff , resistivity gives average temperature
confinement time if density is known
evidence of heating, cooling
NB interpretation difficulties in presence of current drive!
With R, a, κ, BΦ , allows calculation of q: see Operating Limits
Current magnitude sets Bθ , hence poloidal Larmor orbit size:
max runaway electron energy
max fast ion energy (NBH, ICRH)
Necessary Diagnostics

---
Toroidal plasma current (MAST)
Total toroidal current:
Sum of all PF coil and casing currents:
Difference = plasma current:
Necessary Diagnostics

---
Plasma position
Affects:
plasma aperture (hence a, R, q etc)
proximity to stabilising structures
matching to antenna shape and position
matching to probes and viewing lines
conditioning of limiter surfaces
Measured by:
flux loops (in-out, up-down) and saddle coils
refined by Bθ pick-up coil signals
edge Langmuir probes
H detector arrays
reflectometry
Necessary Diagnostics

---
Magnetic diagnostics (Pegasus)
Necessary Diagnostics

---
Plasma position
Accuracy of magnetic diagnostics is also adversely affected by:
errors in effective coil area or N turns
errors in position
errors in orientation
unintended pick-up loops
proximity to ferritic zones
proximity to conducting structures (eddy currents)
coupling to major plasma MHD modes
integrator drift
Test methods should include:
check of temperature and vacuum cycling immunity
pre-installation calibration (up to self-resonant frequency)
“ringing through” each coil connection circuit
pulsing individual poloidal field coils
both directions of plasma current
amplifier/integrator/ADC gains
Necessary Diagnostics

---
Necessary Diagnostics
Plasma position (MAST equilibrium)
Necessary Diagnostics

---
Necessary Diagnostics
Plasma position (MAST equilibrium)
Necessary Diagnostics