The BME Lectures - Tokamak Engineering - “How to Operate a Tokamak” T N Todd
Interferometer
Plasma density is a crucial operating parameter
key parameter defining stable operation window
strongly affects OH confinement
strongly affects RF wave access (ECRH, LHH, AWH…)
strongly affects Neutral Beam shine-through
strong coupling to edge physics
high density, low Te(a)  low sputtering yields
Design considerations
wavelength
avoid refraction losses near OM cut-off
avoid vibration problems when wavelength too short
geometry
vertical (easier to make vibration-proof)
mid-plane (insensitive to plasma radial position)
Necessary Diagnostics

---
Interferometer
Profile relationships
If n = n0 ( 1 - (r/a)2 )
typically with 0.5 <  < 2
then
n0 /n  n / <n>  (1 + )
To raise  :
run at low density (high I/N)
use deep-fuelling pellet injection
reduce edge recycling (e.g. helium GDC between shots)
- -
Necessary Diagnostics

---
Impurity survey spectrometry
Facilitates operational improvements
identify dominant impurities
identify operational problems
“strange” materials e.g. Langmuir probes, forgotten tools
poor vacuum cleanliness
insufficiently conditioned limiter surfaces
corroborate data on Te (ionisation stage burn-through)
spatial profile helps deduce Te(r)
care with validity of coronal equilibrium assumption
Necessary Diagnostics

---
Impurity survey spectrometer (COMPASS-D)
Necessary Diagnostics

---
Stray magnetic fields
Non-resonant, or toroidal average Bθ
causes toroidal magnetic field lines to spiral across the vessel
accelerates losses of initial electrons from the vessel
inhibits electron avalanche
inhibits flux surface closure at low plasma current
so design in a poloidal field null region...
.. in theory m4 but in practice m=2 is OK
Resonant, i.e. with pseudo-helical components
can cause tearing mode locking during current rise phase
possible early disruption
probable waste of volt-secs
sources include
feeder bar stray fields (especially with jointed TF coils)
zones of high magnetic permeability in or near the torus
Plasma Initiation

---
Stray magnetic fields (ITER)
NB octupole
structure of null
Plasma Initiation

---
Gas breakdown and current rise
Gas breakdown is a classical Pashen curve phenomenon
choose a prefill pressure around 10-4 torr
produce a toroidal electric field of about 3V/m
keep stray Bθ / BΦ < 10-4 to avoid prompt electron loss
wait 1-3msecs
Preionisation options
UV lamp (not very effective)
electron gun
ensure electron B drift is into torus from gun location
check emission current daily
ECRH
<10kW is OK
care with impurity production where resonance impacts	vessel surfaces
Reverse plasma current pulse, laser-pellet,	radioactive source….
Plasma Initiation

---
Gas break-down
Plasma Initiation

---
Gas breakdown (MAST)
Vloop
D-mid
D-div
density
Ip
Plasma Initiation

---
Current
Maximum plasma current is limited by n=1 gross MHD instabilities
kink modes
tearing modes
usually m=3, m=2, coupled m=1 and m=2
these are driven by current gradients at the plasma edge and	hence resonate with the edge safety factor qa (or q95 in a	discharge defined by a magnetic separatrix)
qa  5a2 BΦ (1 + κ2) / 2RIp
but you need to do an equilibrium code run for accuracy!
Minimum plasma current is limited by the need to:
support the charge exchange and radiative losses
confine “fast” ions (eg tail of thermal distribution)
provide adequate energy confinement time
Plasma Operating Limits

---
Current
Current magnitude sets density limit, as I/N or Greenwald scaling
Not really Ip / ( nea2) but (<j>/ne)2
Arises due to OH and Prad having similar f (Te, Zeff)
POH/Prad  <j>2 Zeff Te-3/2 /ne2 f (Zeff)Te  -3/2
Hence an indicator of bulk radiative cooling becoming too large
Works for all OH plasma devices between 20eV and 3keV
In tokamaks, radiated power erodes plasma current channel and	destabilises the m=3 or m=2 mode.
Reduction of Zeff does help expand operating limits
Plasma Operating Limits

---
Density
Maximum density is set by disruptive limit, raised by:
better vessel conditioning
limiter conditioning
low-Z vessel and limiter coatings
pure hydrogenic pellet injection
reduces Zeff
raises density profile peaking factor ()
increased auxiliary heating power (if Zeff is kept low)
Minimum density is set by electron slide-away condition
toroidal electric field accelerates all electrons, tail	electrons become collisionless if density is too low
keep EΦ small (helped by clean machine)
keep I/N < 1.5 x 10-13 amp-metres
Consider also the needs of the auxiliary heating system
sufficient line density to absorb neutral beam
RF wave access
Plasma Operating Limits

---
Plasma Operating Limits

---
Pressure
Plasma pressure has no lower limit
The upper limit is set by , i.e normalised to magnetic field pressure.
Ideal kink modes set low-m limits
require q0 > 1 (not generally true!)
most constraining when qa  integer
Ideal ballooning modes set high-m limits
actually limited by FLR effects to m<30
“ballooning” means “ballooning the flux surface perturbation outwards in regions of poor magnetic curvature”
Both have similar parametric dependence:	  4 Ip/a BΦ (%, MA, m, Tesla) or equivalently	  20/qa (%, dimensionless) where  = a/R
Both have resistive analogues with lower thresholds and	non-linear saturation effects clamping achievable pressure
Plasma Operating Limits

---
Plasma pressure
(MAST)
Here, T = <p>/(Bo2/2o)
...but Troyon used:
<p>/<B2/2o>
Plasma Operating Limits
START
MAST
NSTX
Pegasus

---
Plasma duration
Plasma duration is limited by:
OH volt-secs consumption
current drive parameter sustainment (power, density…)
thermal limits of limiters etc
Available flux-swing  is dictated by primary design
small tokamaks
tpulse = ( - 1.5 IL)/ Vloop
large tokamaks
tpulse = ( - 2 - IL )/ Vloop
Performance Predictions

---
Confinement
Tokamak discharges usually begin as OH, subsequently given Paux.
OH confinement is given by scalings such as “TFTR”:	E  10-21 naR2qa0.5 (secs, m-3, m, m)
p is generally about 4 xE
Adding auxiliary heating always (?) degrades confinement
Slide-away discharges (OH or LHeH) can exhibit E > E OH
See “How to Build a Tokamak” or Wesson for E(Paux) scalings
Performance Predictions

---
Confinement
ITER predictions drive strong interest in E(Paux) scalings
Performance Predictions

---
Confinement analysis
The usual equation for confinement time is:	E = W/(Ptot - dW/dt)
But what is	W and what is Ptot?
W (stored energy) should account for:
all particle species
non-Maxwellian distributions (tails)
anisotropic distributions
Ptot (total absorbed power) should account for:
Prad (impurities, ECE, bremstrahlung…)
Pabs (shine through, prompt losses)
POH (remembering all PF sources)
plasma-dissipated changes in inductive stored energy,	Ip2(Lint + Lext)/2
Performance Predictions

---
Radiated power issues
(MAST)
Plasma current
Beam current
Bolometric power
Plasma Performance

---
Operations Planning
Successful planning has to cover many elements
topical experiments
novel experiments
installation of new equipment
politics! (resource constraints, raison d’être)
maintenance
regular
remedial
Try to keep a balance:
programmed focus
unplanned flexibility
Use regular meetings to look ahead:
a few months (eg to suit conferences)
a week (eg to accommodate repair work)
a day (eg to accommodate unavailabilities)
Human Factors

---
Team building
Only people truly in the team will enthuse!
experimental lead physicists
experimental support physicists
diagnosticians
technicians
(theoreticians?)
These people must be present
in all planning meetings
in the control room
preferably in person
maybe by VR, including video links
Otherwise you will encounter considerable operational delays!
Human Factors

---
Safety
Plant safety is covered by good design
known maxima of parameters
rigorous QA during manufacture and installation
engineered interlocks
sound commissioning tests
comprehensive operating procedures
Human safety
Tokamaks feature a wide variety of safety hazards
Safety must have “buy-in” at all staff levels
area access interlocks
standing orders
personal protective equipment (gloves, hats)
management example and enforcement
Human Factors

---
Example tokamak safety issues
This work was funded by the UK DTI and by EURATOM.
Human Factors

---
Example tokamak safety issues
This work was funded by the UK DTI and by EURATOM.
Human Factors

---
Successful tokamak operation requires a wide range of topics to be addressed:
thorough preparation of the machine
at least a minimal set of plasma diagnostics
consideration of gas breakdown and plasma current rise phenomena
respecting the conventional operating limits (usually!)
selecting diagnostics (etc.) that are consistent with predicted performance
recognising how humans really work (and how they do not)
Get most of these right, most of the time,
and you will have a highly productive machine!
Summary

---
MAST plasma evolution (visible light, shot duration ~500ms)
Successful Operation...

---
END
How to Operate a Tokamak

---
End
A giant Edge-Localised Mode in MAST

---
Electrical engineering
Machine Preparation

---
Vacuum and gas systems
Machine Preparation

---
Control system (MAST poloidal fields)
Machine Preparation

---
Control system (JET density feedback)
Machine Preparation

---
Edge Localised Modes
ELMs produce high energy pulses:
Generic “H-Mode” plasma profile:
Plasma Operating Limits
Plasma Pressure

---
Current drive
The power required to drive the toroidal plasma current scales in a similar way for lower hybrid waves and neutral beams:
LHCD
PLHCD  IRn19 (MW, MA, m, m-3)
NBCD
PNBCD  5 IRn19 /TeCosbeam (MW, MA, m, m-3, keV)
NB there are also dependences on Te (and Zeff), details of antennae, beam geometry etc.
Performance Predictions

---
Team building
Human Factors