## Slide 1
Plasma MHD Activity Observations via Magnetics Diagnostics:
Magnetic island Analysis
Frederik Ostyn (UGent)
Daniel Hernández (CICATA-IPN)
Mauricio Rodríguez (US)
GOMTRAIC 2013

## Slide 2
INTRODUCTION
SAFETY FACTOR
MAGNETIC ISLANDS
DETECTION METHOD
FLUCTUATION OF RAW DATA
SPECTROGRAM
SUMMARY
Overview

## Slide 3
Gas confined by magnetics fields
Tokamak (GOLEM)
Major Radius: 0.4 m Minor Radius: 0.1 m
Toroidal Magnetic Field < 0.8 T
Plasma Current: < 8 kA
Discharge Duration: 13 ms
Background Pressure of Vacuum: 10 - 200 mPa
Work Gas: H2
Low density and long connement time.
Fusion in Earth
gas
Introduction
  Plasma in equilibrium*:
  Ψ = const
  p = const
  T = const
  jplasma=const
* circular cross-section and zero Shafranov shift
Helical Shape

## Slide 4
Safety factor
“How many toroidal rotations are neccesary for a single rotation of a magnetic field line in the poloidal direction (2p)”
Depends on the geometry of the machine Major Radius: R=0.4 m Minor Radius: r=0.1 m
At the plasma Edge (r=a)

## Slide 5
Control Room system

## Slide 6
Safety factor: Experimental
Stability of plasma requires the safety factor at the edge (r=a):
2 < qmin(a) < 3
Shot # [-] | UB [V] | UCD [-] | TCD[ms] | PH2[mPa] | Preion[-]
11688 | 500 | 600 | 5000 | 2.07->16.92 (12) | 1
11689 | 400 | 600 | 5500 | 1.69->11.80 (12) | 1
11691 | 500 | 600 | 10000 | 1.71->10.02 (10) | 1
11692 | 500 | 600 | 10000 | 1.72->9.96 (10) | 1
11701 | 400 | 600 | 5000 | 1.63->11.40 (12) | 1
11702 | 400 | 500 | 5000 | 1.60->11.53 (10) | 1
11703 | 400 | 400 | 5000 | 1.60->9.89 (10) | 1
11704 | 400 | 300 | 5000 | 1.61->10.00 (10) | 1
Time(s)

## Slide 7
A magnetic island is a closed magnetic flux tube , bounded by a separatrix , isolating it from the rest of space
The rupture of the assumed initial topology of toroidally nested flux surfaces needed to produce the island which requires the reconnection of magnetic field lines in plasma.
Magnetics Islands (I)

## Slide 8
If a magnetic island appears, heat and particles transport is enhanced due to shorted field lines, and as a result there is a deterioration of pressure, temperature and plasma current profile.
Magnetics Islands (II)
Irrational: Any fluctuation can spread quickly and
homogeneously
Small rational numbers: due to geometrical properties and periodic boundary conditions a plasma wave can live for long time (MHD mode).

## Slide 9
Magnetics Islands (III)
q = m/n=3
q = m/n=2
q = m/n=1
M = 3 mode is closer to the edge and detector. So the signal would be stronger.

## Slide 10: Detection of magnetic island
Magnetic islands are rotating with the plasma in the toroidal direction
Islands deteriorates p, T and j
On GOLEM, p and T measurements are not optimized but can measure j
Measurement of time evolution of poloidal magnetic field
Set of sensors of local magnetic field (for GOLEM 16)

## Slide 11: Bθ measurement coils
Coil # [-] | Polarity [-] | Aeff [cm^2]
1 | - | 68.93
2 | - | 140.68
3 | + | 138.83
4 | + | 140.43
5 | - | 68.59
6 | + | 134.47
7 | - | 134.28
8 | + | 142.46
9 | - | 67.62
10 | + | 142.80
11 | - | 140.43
12 | x | x
13 | x | x
14 | x | x
15 | - | 139.82
16 | - | 139.33
Signal is measured on distribution of local magnetic field sensors

## Slide 12: Fluctuation of Raw Data (I)
Number of oscillation maxima for one period time given time of the mode is equal to m mode number
m=2
T
T
Window of signal from all the sensors

## Slide 13
# 11688
# 11691
# 11692
# 11689
Fluctuation of Raw Data (II)
Oscilations are best visible when island is on radius close to plasma edge

## Slide 14
Shot # [-] | Island Index | Time_d[ms] | Time_u[ms] | m[-] | Comments
11688 | 1 | 16.4 | 16,6 | 2 | Good Signal
11689 | 1 | 14,8 | 15,0 | 2 | Nice
11691 | 1 | 24,0 | 24,2 | 2 | Nice
11691 | 2 | 25,8 | 26 | 3 | Not Very Nice
11692 | 1 | 25,3 | 25,5 | 2 | 
11701 | 1 | 14 | 14,2 | 2 | 
11702 | 1 | 15 | 15,2 | 2 | 
11703 | 1 | 19,2 | 19,4 | 2 | 
11704 | 1 | 21,7 | 21,9 | 1 | 
Fluctuation of Raw Data (III)

## Slide 15
Spectrogram
15
To know the time of MHD mode appears
Look for high peaks in spectrogram (dark red)
The time window where the peaks appear is where to look (black circles)
# 11704, coil 4

## Slide 16
Summary
In a Tokamak the magnetic configuration produces a field in toroidal and poloidal axis, in GOLEM Tokamak this can be controlled remotely
The safety factor in Tokamak GOLEM is determined by
Low values for safety factor are ideal to observe magnetic island
In Tokamak GOLEM MHD studies is by 16 Mirnov coils mounted in a poloidal ring
Number of oscillation maxima for one period time given time of the mode is equal to m mode number
Mode number 2 was observed a lot of times
The spectrograms show the magnitude of the signal in frequency state for each coil of poloidal arrangement
Future work is to process the signal with statistical methods (cross correlation, to get a better analysis)

## Slide 17: Thank you for your attention
Contact: frederik.ostyn@ugent.be
Contact: Mauricio.Rodriguez-Ramos@ipp.mpg.deg
Contact: ingdha@hotmail.com