## Slide 1: 1st Research Coordination Meeting CRP on Network of Small and Medium Size Magnetic Confinement Fusion Devices for Fusion Research
Fuelling and confinement studies on the STOR-M tokamak-F13019
Chijin Xiao
University of Saskatchewan, Canada
Vienna, Oct. 8-11, 2018

## Slide 2: Our Laboratory
Plasma Physics Laboratory, Department of Physics and Engineering Physics, University of Saskatchewan, Canada
Established by Prof H.M. Skarsgard in 1958 and later led by Prof. A. Hirose (1994-2017)

## Slide 3: Professors in PPL
L. Couedel
M. Bradley
C. Xiao
A. Smolyakov
Plasma aided material synthesis and processing
Dusty Plasma
Theoretical Plasma Physics
Tokamak and Compact Torus Dense Plasma Focus

## Slide 4: Main Facilities
STOR-M tokamak
Compact torus injector
Dense plasma focus device
ICP and microwave plasma devices

## Slide 5: STOR-M Tokamak
Construction started in 1984
Operational since 1987
Still active as the only tokamak in Canada today

## Slide 8: Main Axillary Systems and Diagnostics
Feedback position control
Resonant magnetic perturbation coils
AC operation compatible
Lithium wall coating system (Physical Vapor deposition)
4-mm interferometer
SXR pin-hole cameras
2-cm reflectometer
Mirnov coil arrays and electric probes
IDS for toroidal flow measurement

## Slide 9: STOR-M experiments/expertise
Improved confinement induced by
  Electrode/limiter biasing (early 1990s)
  Turbulent heating
  Compact torus injection
AC operation (O. Mitarai)
Compact Torus Injector (mid 1990 – now)
Resonant Magnetic Perturbations

## Slide 10: Main Research Activities Proposed, 1
Revisit the improved confinement in the STOR-M tokamak
  Triggering techniques: Electrode biasing, CT injection, RMP, turbulent heating
  New: Combined with Lithium coating of the chamber wall
  Sustainment: Combine different techniques and or repetitive triggering to sustain the improved confinement phase
  Mechanism: Correlate the improved confinement with magnetic and density fluctuation properties and plasma flow measurement.

## Slide 11: Main Research Activities Proposed, 2
Compact Torus injection into the STOR-M tokamak
  Continue studies of momentum injection by CT injection
  Try to understand momentum transport in STOR-M (Magnetic breaking and transport)
  Repetitive CT operation (up to 100 Hz)
  Multiple CT injection into a single STOR-M discharge

## Slide 12: Electrode Biasing

## Slide 13: H-Bridge Circuit
18
LC load
R load

## Slide 14
Lithium evaporator

## Slide 15
Tangential CT injection is a unique feature of USCTI/STOR-M experiments

## Slide 16
Density ↑
Hα decrease
MHD Fluctuations ↓
Floating potential fluctuations ↓
Energy confinement time ↑
CT injection induced H-mode like discharge

## Slide 17: Flow modification by CT injection
vt
vt
Normal plasma current and flow direction
Reversed plasma current and flow direction

## Slide 18: Understand Momentum Injection and Transport
Magnetic Resonant Perturbation along also modifies the toroidal flow velocity
CT injection suppresses magnetic fluctuations and modifies the flow
Need to quantify the effects of magnetic breaking and the momentum injection.
Need to understand momentum transport in STOR-M

## Slide 19: Repetitive CT Operation
Repetitive CT injection is needed for steady state CT operation.
ITER size tokamak required fueling rate of 100 Hz
PPL at UofS has already produced a burst of 3 CTs at about 10 Hz
Will try to increase the rate to 100 Hz
Then to demonstrate injection of 3 CTs into a single STOR-M discharge.

## Slide 20: 1st Year Activities Planned
Electrode biasing under the following conditions
  Characterization of STOR-M discharges with Lithium coated wall
  Electrode biasing experiments with Lithium coated wall
CT operation/injection
  Increase repetitive CT operation to 30Hz

## Slide 21: 2nd -4th Year Activities Planned, 1
Improved confinement studies
  Rectangular biasing voltages pulse with different polarities or sinusoidal waveform
  Inject CT into Ohmic H-mode discharges
  Combine different H-mode triggering techniques to sustain the improved confinement phase
  Analyze fluctuations measured by magnetic probe arrays, Langmuir Probes and reflectometer.
  Effects of velocity shear on the anomalous transport

## Slide 22: Collaboration (inputs)
Theoretical studies of plasma flow and momentum transport
Data analyses software/codes
Edge plasma diagnostics expertise
Data sharing (STOR-M is adopting MDSPlus database)

## Slide 23: Thanks!

## Slide 24: Extra slides

## Slide 25: Flow modification by CT injection (normal tokamak current direction)
Changes of the flow velocity are along CT injection direction
(CT momentum is approximately 10 times the plasma rotation)
vt

## Slide 26: Flow modification by CT injection (reversed tokamak current direction)
Reversed plasma flow direction
Changes in flow velocity are still along CT injection direction
vt

## Slide 27: Experimental Setup -RMP
m/n=2/1 helical coils to suppress the dominant mode
1st
2nd bank
bank

## Slide 28: Content of the presentation
Introduction + background of the institute on the proposed activities
Facilities / expertise available
Work to be done (1 year + 2-4 year):
  Activities + task + deliverables+ comments
  Tasks where collaboration is needed (one page for this)
Final goal of the activities described
Input of the activities proposed into the final goal of the Coordinated Research Project
Maximum number of slides: 25